## Slide 1: Fault-Tolerant Quadrotor Control
PROJECT 6 · INTRODUCTION TO UAV DESIGN
A quadrotor that stays under control when one motor drops to 50% RPM mid-mission
Demonstrated on a Crazyflie 2.1 nano quadrotor
Team LUGER
Batta Venkata Shashank · Nelagonda Pavaneswar · Jetty Jithendra · Vineel Sai Reddy
Hemanth · Shaik Babu · Prasad
weak motor
Notes: Good morning. We're Team LUGER, working on Project 6, fault-tolerant quadrotor control. In one line: we're making a quadrotor keep flying its path even when one motor is limited to half its normal speed. That's the orange motor here. Our platform is a Crazyflie nano quadrotor. We'll cover our objectives, our solution framework, the deliverables we're committing to, and the components we're using.

## Slide 2: Problem statement
1
Design and build a quadrotor that stays under control after a partial loss of motor performance
2
During an autonomous waypoint mission, one motor is limited externally to 50% of its maximum RPM
3
The controller is told which motor: fault detection is not required
4
The controller must adapt to the reduced actuator capability
5
It then continues the mission, or ends it safely and lands, under control throughout
Our platform
We cannot build a quadrotor within the project time, so we fly a Crazyflie 2.1 (27 g, open firmware) as the airframe.
What is ours
The fault-tolerant controller, the fault interface and the mission logic. None of them depend on the airframe.

## Slide 3: Objectives
1
Fly a quadrotor autonomously around a rectangular path, with all motors healthy (our baseline)
2
Partway through, one motor is limited to 50% RPM and the controller is told which one
3
Adapt the controller so the drone stays under control
4
Then finish the rectangle, or end the mission and land safely
5
Log every flight, so each result is backed by measured data
Demo
Outdoors on a football ground, one rectangular path. Platform: Crazyflie.
Out of scope
Detecting the fault. The brief says we are told which motor is weak and when.
Notes: We have five objectives, all from the project brief. One: fly a quadrotor autonomously around a rectangle, using a Crazyflie as our platform, with all motors healthy. That's our baseline, and every result after the fault is compared against it. Two: partway through, one motor is limited to 50% of its maximum RPM, and the controller is told which one. Three: the controller adapts so the drone stays under control. Four: it then finishes the rectangle, or ends the mission and lands safely. Five: every flight is logged, so each claim is backed by data. The demo is outdoors on a football ground. Detecting the fault is out of scope: the brief says we're told which motor and when.

## Slide 4: Why this is hard
25%
of normal thrust is left on the weak motor
thrust ∝ RPM², so 0.5² = 0.25
4 : 1
thrust-to-weight needed to stay level and hold heading
each motor must carry ¼ of the weight
1.7–2.2 : 1
what a Crazyflie 2.1 has (27–29 g)
12.2 g per motor as rated by Bitcraze,
up to ≈16 g on a full battery (to be measured)
So the weak motor cannot hold up its corner.
We give up heading control (yaw): the drone spins, while our controller keeps it level and on the path (Mueller & D'Andrea; Sun et al.). It then has 2.5 motors' worth of thrust, so it needs at least 1.8 : 1 to keep flying: a Crazyflie 2.1 is at that limit, and below it the drone lands safely instead.
Notes: Here's why this is hard. Propeller thrust goes with the square of its speed, so half the RPM leaves only a quarter of the thrust. To stay level and keep its heading, every motor must carry a quarter of the weight. The weak motor can only do that if the drone's thrust-to-weight ratio is at least 4 to 1. Our platform, a Crazyflie, has about 2.2 to 1 for the standard model and about 3.5 to 1 for the Brushless. So on our drone, the weak motor can't hold up its corner. The answer from the research literature is to give up heading control: the drone spins, and we keep it level and on the path.

## Slide 5: Key idea: let it spin, keep it level
10.4 g
carries more
3.1 g
weak, at max
3.1 g
matches
10.4 g
carries more
Example: Crazyflie 2.1, 27 g.
Hover needs 6.75 g per motor; max is 12.2 g (Bitcraze rating).
The weak motor gives its maximum
about 3.1 g, a quarter of its normal maximum
Its diagonal partner matches it
equal diagonals keep the drone level
The other two carry the rest
10.4 g each: 86% of their 12.2 g limit, little left to steer
Heading is given up
the spin directions no longer cancel, so the drone spins; we control only where its thrust points
Notes: This is the key idea, shown on a standard Crazyflie. In hover each motor needs 6.75 grams, but the weak motor can only give about 3.75. Its diagonal partner drops to match it, because equal diagonals keep the drone level. The other two motors carry the rest, about 9.75 grams each, well within their 15 gram limit. The total is still 27 grams. The cost is heading: diagonal motors spin the same way, so the twisting forces no longer cancel and the drone spins. We stop controlling which way it faces and control only which way its thrust points.

## Slide 6: Architecture: ground station and drone
GROUND STATION · laptop, Python
DRONE · onboard (Crazyflie firmware), C
Mission
the rectangle path, step by step
Position MPC
plans the motion, 50–100 times a second
Health check · logging
decide: continue or land
INDI attitude control
keeps the tilt right, 500 times a second
WLS motor allocation
shares the work across the 4 motors
4 motors
speeds set by WLS
State estimator
IMU + positioning
setpoints, radio
telemetry
fault message
Orange outline = code we write or change. The fast loop stays on the drone: radio delay (~10 ms) is too slow for 500 Hz stabilisation.
Notes: This is our architecture. Work is split between the laptop and the drone. On the laptop: the mission, which is the rectangle and a small state machine; a position MPC that plans the motion; and the health check and logging. The laptop sends setpoints over the radio link and receives telemetry back. On the drone, at 500 times a second: INDI attitude control, which we adapt from the drone's firmware, and WLS motor allocation, which replaces the stock mixer. The orange boxes are code we write or change. The fault message goes from the laptop to the drone. Why not run everything on the laptop? The radio adds around 10 milliseconds of delay, too slow for stabilising a spinning drone, so the fast loop has to stay onboard.

## Slide 7: Three control layers
1 · Position MPC
Model Predictive Control
Laptop · 50–100 times a second
Plans the next second of motion along the rectangle and keeps every command within thrust and tilt limits.
Why we need it
After the fault, limits are the whole problem. It also estimates steady wind and leans into it.
2 · INDI attitude control
Incremental Nonlinear Dynamic Inversion
Drone · 500 times a second
Measures how the rotation is actually changing and corrects the difference, step by step.
Why we need it
The weak motor and wind gusts show up as measured disturbances and get cancelled, without an exact model.
3 · WLS motor allocation
Weighted Least Squares
Drone · 500 times a second
Splits lift and turning effort across the 4 motors, each within its own limit. Priority: level, then lift, then heading.
Why we need it
The stock mixer assumes all 4 motors are equally strong.
Each layer feeds the next: MPC → INDI → WLS → motors.
Notes: There are three control layers. First, the position MPC on the laptop. It looks about a second ahead, plans the motion along the rectangle, and never plans a move the damaged drone can't make. It also estimates a steady wind and leans into it, which matters outdoors. Second, INDI on the drone. Instead of trusting a model, it measures how the rotation is actually changing and corrects the difference. A weak motor or a gust just appears as a measured disturbance, and INDI cancels it. Third, WLS allocation. It splits the work across the four motors, respecting each motor's own limit, with a clear priority: stay level first, then hold height, and heading last. We need it because the stock mixer assumes every motor is equally strong.

## Slide 8: What changes when the fault message arrives
Evaluator caps motor k at 50% RPM
Laptop sends “motor k at 50%” over the radio link
Controller switches to fault mode, ramping over ~0.2 s
What changes | Normal flight | After the fault
Motor k limit | 100% of max thrust | 25% of max thrust
Heading (yaw) | Held | Released: control thrust direction only
Allocation priority | Level, lift, heading | Level, lift (heading weight ≈ 0)
MPC limits | Full thrust, normal tilt and speed | Thrust ≈ 2.5 of 4 motors; lower tilt and speed
In tests, one laptop command applies the cap and sends the message together. 50% RPM = 25% thrust, calibrated on a thrust stand.
Notes: Here's exactly what happens at the fault. The evaluator caps motor k at 50% RPM, and our laptop sends the message 'motor k is at 50%' over the radio link. The controller switches to fault mode, ramping over about 0.2 seconds so nothing jumps. Four things change. Motor k's limit drops to 25% of its maximum thrust. Heading is released, and we control only the thrust direction. The allocation stops spending effort on heading. And the MPC tightens its limits: about two and a half motors' worth of thrust instead of four, with lower tilt and speed. In our own tests, one laptop command applies the cap and sends the message together. Since half RPM means a quarter thrust, we calibrate the cap on a thrust stand.

## Slide 9: After the fault: step by step
1 · Fault applied
motor k capped at 50% RPM (25% thrust)
2 · Message received
laptop → drone: “motor k at 50%”
3 · Switch to fault mode
k limit 25% · yaw released · MPC limits tightened
4 · Spin, stay level
INDI + WLS hold the tilt; heading drifts
5 · Settle
hold position for 2–3 s
6 · Health check
tilt · position · battery · wind
all OK
Continue the rectangle
at half speed, then land at A (our goal)
any check fails
Land where it is
slow, controlled descent
At any time: sudden drop
level + full thrust; too low or flipped → cut motors
Both endings meet the brief. Finishing the rectangle is our goal.
Notes: This flowchart shows exactly what happens after the fault. One: the fault is applied, so motor k is capped at 50% RPM, which leaves 25% of its thrust. Two: the laptop sends the drone the message 'motor k is at 50%'. Three: the controller switches to fault mode: motor k's limit drops to 25%, heading is released, and the MPC limits are tightened. Four: the drone starts to spin, but INDI and WLS allocation keep it level. Five: it holds position for two to three seconds to settle. Six: the health check looks at tilt, position, battery and wind. If everything is OK, it continues the rectangle at half speed and lands at A, which is our goal. If any check fails, it lands where it is. Both endings meet the brief. And at any time, if there's a sudden drop, it levels and uses full thrust, and if it's too low or upside down it cuts the motors.

## Slide 10: Demo mission: one rectangle
A
B
C
D
fault
take-off and landing at A
Size set by the positioning system: about 2 m sides with Flow deck, larger with Loco anchors. Height 0.5–1 m.
1
Baseline flight
A → B → C → D → A, all motors healthy
2
Fault flight
same path; fault applied on B → C
3
Settle
hold position for 2–3 s
4
Health check
tilt, position error, battery, wind
5
Decide
pass: finish at half speed, land at A · fail: land where it is
Notes: The demo is one rectangle. First, a baseline flight: A, B, C, D and back to A with all motors healthy. Then a second flight on the same path, and partway along B to C the fault is applied. The drone holds position for two to three seconds while the spin settles. Then it runs a health check: tilt, position error, battery and wind. If everything passes, it finishes the rectangle at half speed and lands at A. If anything fails, it lands where it is, which the brief also accepts. The size of the rectangle depends on the positioning system: about 2 metres a side with the Flow deck, larger with Loco anchors.

## Slide 11: Flying outdoors, and extreme cases
Football ground
Position: our drone has no GPS and Lighthouse fails in sunlight, so we use Loco UWB anchors around the path (Flow deck as fallback)
Wind: INDI cancels gusts; MPC estimates steady wind and leans into it
Fly in calm hours, at low height, over soft grass, from a flat take-off pad
Extreme cases (in progress)
Example: a sudden drop after completing a lap
Detect: fast height loss or near-zero g from the accelerometer and height estimate
Respond: level the drone and use all available thrust to stop the fall
If too low or upside down: cut motors before impact (firmware tumble check)
Laptop kill switch available at all times
Notes: Two practical points. First, the demo is outdoors on a football ground. Our drone has no GPS, and the Lighthouse system fails in sunlight, so we plan to use Loco UWB radio anchors around the path, with the Flow deck as a fallback. Wind is the main risk for a 30 gram drone. INDI cancels gusts the same way it cancels the motor fault, and the MPC estimates a steady wind and leans into it. We'll fly in calm hours, low, over grass. Second, extreme cases, which we're still working on. For example, if the drone suddenly drops after completing a lap: we detect fast height loss or near-zero g, level the drone and use all available thrust to stop the fall. If it's too low or upside down, the motors are cut before impact, using the firmware's tumble check. A kill switch on the laptop is always available.

## Slide 12: How we will build and test it
1
Python simulation
Our Python simulator: prove the algorithm with one motor capped
2
Firmware simulation
CrazySim: run our real C code before flying
3
Baseline flights
rectangle with all motors healthy; logs saved
4
Fault tests
low height over grass; fault on, then off
5
Full demo
football ground: baseline + fault flight
Fallback levels after the fault, so every stage gives a working demo:
Level A
spin and land safely
Level B
spin and hold position
Level C
spin and finish the rectangle
Notes: This is how we'll build it, in five steps. First, a Python simulation in PyBullet, where we cap one motor and prove the algorithm works. Second, CrazySim, which runs the real Crazyflie firmware, so we can test our actual C code before flying. Third, baseline flights of the rectangle with all motors healthy. Fourth, fault tests at low height over grass. Fifth, the full demo on the football ground. We also have three fallback levels after the fault. Level A: spin and land safely, which already meets the brief. Level B: spin and hold position. Level C, our goal: spin and finish the rectangle. Each stage leaves us with a working demo.

## Slide 13: Progress so far (simulation)
Where | Test | Result
Python sim | 27 g quadrotor, M1 at 50% RPM on B → C | Stock flips; ours finishes the rectangle
Python sim | Same, with 2 m/s wind | Ours finishes; Kalman filter finds the wind force (20 mN)
CrazySim | Crazyflie 2.1 Brushless, M1 at 50% RPM | Stock crashes; ours finishes the rectangle
CrazySim | Crazyflie 2.1 (27 g), M1 at 50% RPM | Ours lands level at 0.6 m/s; stock falls at 2.2 m/s
CrazySim | Crazyflie 2.1, M1 at half thrust, hover | Ours stays level (2 deg); stock crashes
CrazySim | Crazyflie 2.1, M1 switched off | Ours comes down upright; stock flips
CrazySim runs the real Crazyflie firmware with our controller in C. Next: thrust test, then staged flights on the real drone.

## Slide 14: Deliverables
# | Deliverable | How we will show it
D1 | Quadrotor and propulsion integration | Crazyflie + positioning + radio + our app; thrust calibration
D2 | Stable baseline autonomous flight controller | Position and attitude logs in healthy flight
D3 | Autonomous waypoint navigation | Rectangle flown; planned vs flown path plot
D4 | Interface for receiving the fault notification | Logs show the switch to fault mode on the message
D5 | Fault-tolerant control strategy | INDI + WLS allocation; simulation results vs stock controller
D6 | Control reallocation and reconfiguration | Motor commands and limits, before vs after the fault
D7 | Baseline and post-fault flight demonstrations | Two logged flights on the football ground
D8 | Continue the mission or end it safely | A post-fault flight that finishes the rectangle or lands
D9 | Flight logs, data and technical report | Raw logs, analysis scripts and report
D1–D8 follow the project brief one to one; D9 covers the common deliverables.
Notes: These are the deliverables we're committing to. D1 to D8 follow the brief one to one, and the right column says how we'll prove each one. D1 is the Crazyflie integrated with positioning, the radio link and our firmware app, plus thrust calibration. D2 and D3 are normal flight: a stable baseline controller and the rectangle mission. D4 to D6 are the fault handling: the notification interface, the fault-tolerant strategy compared against the stock controller in simulation, and the reallocation and reconfiguration. D7 is the pair of demo flights. D8 is the decision after the fault: finish or land safely. D9 is the logs, data and report.

## Slide 15: Stretch goals and scope
Stretch goals
If time allows; not committed
Finish the full rectangle in every fault trial
Recover from a sudden drop (extreme case)
Compare the stock controller with ours in real flight (committed in simulation only)
Out of scope
Not part of this project
Detecting or identifying the fault (excluded by the brief)
Other faults: sensor failures; a fully stopped motor (simulation only)
Our commitment after the fault: finish the rectangle or land safely, as the brief allows.
Notes: To be clear about scope. These stretch goals are things we'll try if time allows, but we're not committing to them: finishing the full rectangle in every fault trial, recovering from a sudden drop, and comparing the stock controller against ours in real flight, which we commit to in simulation only. Out of scope: detecting the fault, which the brief excludes, and other faults like a fully stopped motor or a sensor failure. Our commitment after the fault is to finish the rectangle or land safely, as the brief allows.

## Slide 16: Components
Hardware
Component | Role
Crazyflie 2.1 nano quadrotor | Stands in for a custom-built quadrotor (from the lab); runs our control code
Loco deck + UWB anchors | Tells the drone where it is outdoors (Flow deck as backup)
Crazyradio USB dongle | Radio link: path commands, fault message, flight logs
Spare batteries, propellers | Several test flights per session
Software
Component | Role
Crazyflie firmware (C) | The drone's built-in software; we add our controller to it
cflib (Python) | Sends the path and fault message, records the logs
CasADi / acados | Solves the MPC on the ground station
Our WLS solver (C) | Motor sharing; checked against our Python version
Our Python simulator, CrazySim | Simulators to test before flying
All software is open source. The drone is provided, so there is no hardware purchase beyond spares.
Notes: Our components. Hardware: the Crazyflie nano quadrotor from the lab, which runs our control code; a Loco positioning deck with UWB anchors, which tells the drone where it is outdoors, with the Flow deck as a backup; the Crazyradio dongle, our radio link to the drone; and spare batteries and propellers. Software: the Crazyflie firmware, which we extend with our app containing INDI, WLS and the fault mode; cflib in Python for the mission, fault message and logging; CasADi or acados for the MPC on the laptop; the WLS solver from Paparazzi, ported to our app; and PyBullet and CrazySim for simulation. Everything is open source.

## Slide 17: Summary
Problem
Keep a quadrotor under control on an autonomous mission when one motor drops to 50% RPM (25% of its thrust), then continue the mission or land safely.
Approach
Give up heading and let it spin. MPC on the laptop plans within limits; INDI and WLS allocation on the drone keep it level.
Demo
One rectangle on a football ground with a Crazyflie 2.1: a baseline flight, then a fault flight that finishes or lands safely.
Thank you. Questions welcome.
Notes: To sum up. The problem: one motor at half speed leaves a quarter of its thrust, and a small quadrotor then can't stay level and hold its heading. Our approach: give up heading and let it spin, with MPC on the laptop planning within the new limits, and INDI with WLS allocation on the drone keeping it level. The demo: one rectangle on the football ground, a baseline flight and a fault flight that finishes or lands safely. Thank you, we're happy to take questions.